## Slide 1: 第十四章 IP访问控制列表

## Slide 2: 为什么要使用访问列表
172.16.0.0
172.17.0.0
Internet
  管理网络中逐步增长的 IP 数据
  当数据通过路由器时进行过滤
Notes: Slide 2 of 2
Purpose:
Emphasize: Access list is a mechanism for identifying particular traffic. One application of access list is for filtering traffic into or out of a router interface.

## Slide 3: 访问列表的应用
  允许、拒绝数据包通过路由器
  允许、拒绝Telnet会话的建立
  没有设置访问列表时，所有的数据包都会在网络上传输
虚拟会话 (IP)
端口上的数据传输
Notes: Slide 1 of 1
Purpose: This figure illustrates common uses for IP access lists.
Emphasize: While this chapter focuses on IP access lists, the concept of access lists as mechanisms to control traffic in a network applies to all protocols.
Note: An improved security solution is the lock-and-key access feature, which is available only with IP extended access lists. Lock-and-key access allows you to set up dynamic access lists that grant access per user to a specific source/destination host through a user authentication process. You can allow user access through a firewall dynamically, without compromising security restrictions.
Transition: The following figure is the first of a 3-layer build that presents other uses of access lists specific to Cisco IOS features.

## Slide 4: 访问列表的其它应用
Queue List
优先级判断
基于数据包检测的特殊数据通讯应用
Notes: Slide 1 of 3
Purpose: This figure is the first of a 3-layer sequence. This layer presents the uses of access lists to prioritize and sort traffic for priority and custom queuing.
Emphasize: Access lists are used to define input traffic to other technologies such as priority and custom queuing and to control the transmission of packets on serial interfaces.
Note: NAT also uses access-list.
Transition: The following figure is layer 2 of this build and adds DDR as a technology supported by access lists.

## Slide 5: 访问列表的其它应用
Queue List
优先级判断
按需拨号
基于数据包检测的特殊数据通讯应用
Notes: Slide 2 of 3
Purpose: This figure is layer 2 of the build sequence.
Emphasize: Access lists are used to define input traffic to select the interesting traffic that initiates a DDR connection. DDR will be covered in the ISDN chapter.
Transition: The following figure is the last layer of the build and adds route filtering.

## Slide 6: 访问列表的其它应用
路由表过滤
Routing Table
Queue List
优先级判断
按需拨号
基于数据包检测的特殊数据通讯应用
Notes: Slide 3 of 3
Purpose: This figure is the last layer of the build for other uses of access lists.
Emphasize: Access lists are used to define input traffic for route filtering to restrict the contents of routing updates.
Transition: The following figure is a 2-layer build to show the difference between inbound and outbound access lists.

## Slide 7: 什么是访问列表--标准
  标准
    检查源地址
    通常允许、拒绝的是完整的协议
Outgoing
Packet
E0
S0
Incoming
Packet
Access List Processes
Permit?
Source
Notes: Slide 1 of 3
Purpose:
Emphasize: This is a 3 layers slide. The first layer describe a Standard IP access list. The second layer describe an Extended IP access list. The third layer shows that an access list can be applied as an input or output access list on an interface.

## Slide 8: 什么是访问列表--扩展
  标准
    检查源地址
    通常允许、拒绝的是完整的协议
  扩展
    检查源地址和目的地址
    通常允许、拒绝的是某个特定的协议
Outgoing
Packet
E0
S0
Incoming
Packet
Access List Processes
Permit?
Source
and Destination
Protocol
Notes: Slide 2 of 3
Purpose: Describe IP extended access list.
Emphasize:

## Slide 9: 什么是访问列表
  标准
    检查源地址
    通常允许、拒绝的是完整的协议
  扩展
    检查源地址和目的地址
    通常允许、拒绝的是某个特定的协议
  进方向和出方向
Outgoing
Packet
E0
S0
Incoming
Packet
Access List Processes
Permit?
Source
and Destination
Protocol
Notes: Slide 3 of 3
Purpose: Describe inbound versus outbound access list on an interface.
Emphasize:

## Slide 10: 出端口方向上的访问列表
Inbound Interface
Packets
N
Y
Packet Discard Bucket
Choose
Interface
N
Access
List ?
Routing
Table Entry ?
Y
Outbound Interfaces
Packet
S0
Notes: Slide 1 of 3
Purpose: This figure (One of three layers) shows in more detail how an outbound access lists operate in a router.
Emphasize:
Transition: Shows packets coming in an inbound interface. This portion of the flowchart illustrates generic packet handling with or without access lists. The key outcome for the next layer is knowing which interface on the routing table indicates the best or next path.
Is an access list associated with the interface? If not, the packet can route directly, for example, out the upper outgoing interface (the upper arrow). Note: The graphic does not mean that only interfaces with no access group can output packets; based on source and destination addresses, and other parameters, other packets could also pass the access list and be routed out on an interface.

## Slide 11: 出端口方向上的访问列表
Outbound Interfaces
Packet
N
Y
Packet Discard Bucket
Choose
Interface
Routing
Table Entry ?
N
Packet
Test
Access List
Statements
Permit ?
Y
Access
List ?
Y
S0
E0
Inbound Interface
Packets
Notes: Slide 2 of 3
Purpose:
Emphasize: Shows the larger diamond. It contains words to summarize access list statements and permit/deny logic. This layer illustrates a permitted packet now sent to the outbound interface buffer for output (the lower arrow).

## Slide 12: 出端口方向上的访问列表
Notify Sender
If no access list statement matches then discard the packet
N
Y
Packet Discard Bucket
Choose
Interface
Routing
Table Entry ?
N
Y
Test
Access List
Statements
Permit ?
Y
Access
List ?
Discard Packet
N
Outbound Interfaces
Packet
Packet
S0
E0
Inbound Interface
Packets
Notes: Slide 3 of 3
Purpose:
Emphasize: Shows a deny result of the access list test. Now the packet is discarded into the packet discard bucket. The unwanted packet has been denied access to the outbound interface.
The Notify Sender message shows a process like ICMP, returning an “administratively prohibited” message back to the sender.

## Slide 13: 访问列表的测试：允许和拒绝
Packets to interfaces
in the access group
Packet Discard
Bucket
Y
Interface(s)
Destination
Deny
Deny
Y
Match
First
Test
?
Permit
Notes: Slide 1 of 4
Purpose:
Emphasize: This graphic explains in more detail the processes access list statements perform. Use the graphic’s diamond expanded from an earlier page to show individual access list statements.
Shows packets coming into the large diamond. It represents an expanded graphical view from the previous page. Inside, smaller diamonds represent access list statements. They occur in sequential, logical order. Tell students the graphic represents a single access list. There can be only one access list per protocol per per direction per interface.

## Slide 14: 访问列表的测试：允许和拒绝
Packets to Interface(s)
in the Access Group
Packet Discard
Bucket
Y
Interface(s)
Destination
Deny
Deny
Y
Match
First
Test
?
Permit
N
Deny
Permit
Match
Next
Test(s)
?
Y
Y
Notes: Slide 2 of 4
Purpose:
Emphasize: Adds the next test diamond.

## Slide 15: 访问列表的测试：允许和拒绝
Packets to Interface(s)
in the Access Group
Packet Discard
Bucket
Y
Interface(s)
Destination
Deny
Deny
Y
Match
First
Test
?
Permit
N
Deny
Permit
Match
Next
Test(s)
?
Deny
Match
Last
Test ?
Y
Y
N
Y
Y
Permit
Notes: Slide 3 of 4
Purpose:
Emphasize: Adds the third diamond as the next test.
Discuss the logical, ordered testing of packet conditions. One recommendation for the sequence of access list statements begins with the most specific of conditions to match at the beginning of the list; then continue with matches involving a larger group, such as entire subnets or networks. Finish with statements matching still larger groups.

## Slide 16: 访问列表的测试：允许和拒绝
Packets to Interface(s)
in the Access Group
Packet Discard
Bucket
Y
Interface(s)
Destination
Deny
Y
Match
First
Test
?
Permit
N
Deny
Permit
Match
Next
Test(s)
?
Deny
Match
Last
Test ?
Y
Y
N
Y
Y
Permit
Implicit
Deny
If no match
deny all
Deny
N
Notes: Slide 4 of 4
Purpose:
Emphasize: Shows the implicit “deny all.” Describe the final access list test to match any packets not covered by earlier access list statements. All remaining packets match the “Implicit Deny” and are discarded into the bit bucket.

## Slide 17: 访问列表配置指南
  访问列表的编号指明了使用何种协议的访问列表
  每个端口、每个方向、每条协议只能对应于一条访问列表
  访问列表的内容决定了数据的控制顺序
  具有严格限制条件的语句应放在访问列表所有语句的最上面
  在访问列表的最后有一条隐含声明：deny any－每一条正确的访问列表都至少应该有一条允许语句
  先创建访问列表，然后应用到端口上
  访问列表不能过滤由路由器自己产生的数据
Notes: Slide 1 of 1
Purpose:
Emphasize:

## Slide 18: 访问列表设置命令
Step 1: 设置访问列表测试语句的参数
access-list access-list-number { permit | deny } { test conditions }
Router(config)#
Notes: Slide 1 of 2
Purpose:
Emphasize: This graphic give your students a simplified perspective on how to use the two generalized commands in an access list process.
Layer 1—Shows the general form of the global access list command. This declares the number of the list (which indicates the protocol and type of the list), the permit or deny treatment for packets that pass the test conditions, and the one or more test conditions themselves. In practice, you enter one or more of these statements.

## Slide 19: 访问列表设置命令
Step 1:设置访问列表测试语句的参数
Router(config)#
Step 2: 在端口上应用访问列表
{ protocol } access-group access-list-number {in | out}
Router(config-if)#
  IP 访问列表的标号为 1-99 和 100-199
access-list access-list-number { permit | deny } { test conditions }
Notes: Slide 2 of 2
Purpose:
Emphasize: Layer 2—Adds the general form of the interface command. This links the previously specified interface to a group that will handle its packet for the protocol in the manner specified by the global access list statements.
It can help student understanding to learn a generalized command as a simplified template common to most access list processes. However, the details for specific access lists vary widely.
As you present the global access list command material that follows in this chapter, return to the template term “test conditions” if it helps your students associate variations to the general elements of this model.
Emphasize that “test conditions” is an abstraction for this course. Use this abstraction as a generalization to assist teaching and learning. The words “test conditions” are not a Cisco IOS argument or parameter.
Cisco IOS software also offers many variations for the second interface command. As you present these variations, refer your students to the template term “access group” and emphasize how each variation performs a link of the access list test conditions met and the interfaces that packets can use as a result.

## Slide 20: 如何识别访问列表号
编号范围
访问列表类型
IP
1-99
Standard
  标准访问列表 (1 to 99) 检查 IP 数据包的源地址
Notes: Slide 1 of 3
Purpose:
Emphasize: This graphic orients your students to the common numbering classification scheme.
Layer 1—Shows the IP standard access lists and the number ranges for these types of access lists.

## Slide 21: 如何识别访问列表号
编号范围
访问列表类型
IP
1-99
100-199
Standard
Extended
  标准访问列表 (1 to 99) 检查 IP 数据包的源地址
  扩展访问列表 (100 to 199) 检查源地址和目的地址、具体的 TCP/IP 协议和目的端口
Notes: Slide 2 of 3
Purpose:
Emphasize: Layer 2—Adds the IP extended access lists and the number ranges for these types of access lists. These are the most commonly used form of access list.
This layer also adds the method for identifying IP access lists using an alphanumeric name rather than a number. An IP named access list can refer to either a standard or an extended IP access list.

## Slide 22: 如何识别访问列表号
编号范围
1-99 1300-1999
Name (Cisco IOS 11.2 and later)
100-199 2000-2699
Name (Cisco IOS 11.2 and later)
Standard
Named
访问列表类型
  标准访问列表 检查 IP 数据包的源地址
  扩展访问列表 检查源地址和目的地址、具体的 TCP/IP 协议和目的端口
  其它访问列表编号范围表示不同协议的访问列表
Extend
Named
Notes: Slide 3 of 3
Purpose:
Emphasize: Layer 3—Adds the Novell IPX access lists covered in the IPX chapter and the number ranges for these types of access lists. As of Release 11.2.4(F), IPX also supports named access lists.
Point out that number ranges generally allow 100 different access lists per type of protocol. When a given hundred-number range designates a standard access list, the rule is that the next hundred-number range is for extended access lists for that protocol.
Exceptions to the numbering classification scheme include AppleTalk and DECnet, where the same number range can identify various access list types.
For the most part, number ranges do not overlap between different protocols.
Note: With IOS 12.0, the IP access-lists range has been expanded to also include:
<1300-1999> IP standard access list (expanded range)
<2000-2699> IP extended access list (expanded range)

## Slide 23: 通配符掩码指明特定的主机
  例如 172.30.16.29 0.0.0.0 检查所有的地址位
  可以简写为 host (host 172.30.16.29)
Test conditions: Check all the address bits (match all)
172.30.16.29
0.0.0.0
(checks all bits)
An IP host address, for example:
Wildcard mask:
Notes: Slide 1 of 1
Purpose:
Emphasize: This graphic shows students how to use the host abbreviation in the extended access list wildcard mask.
This abbreviation means check the bit value in all bit positions, which has the effect of matching only the specified IP host address in all bit positions.

## Slide 24: 通配符掩码指明所有主机
  所有主机: 0.0.0.0 255.255.255.255
  可以用 any 简写
Test conditions: Ignore all the address bits (match any)
0.0.0.0
255.255.255.255
(ignore all)
Any IP address
Wildcard mask:
Notes: Slide 1 of 1
Purpose:
Emphasize: This graphic shows students how to use the wildcard any abbreviation.
This abbreviation means ignore any bit value in all bit positions, which has the effect of matching anything in all bit positions.

## Slide 25: 通配符掩码和IP子网的 对应
Check for IP subnets 172.30.16.0/24 to 172.30.31.0/24
Network .host
172.30.16.0
0
0
0
1
0
0
0
0
Wildcard mask: 0 0 0 0 1 1 1 1
|<---- match ---->|<----- don’t care ----->|
0 0 0 1 0 0 0 0 = 16
0 0 0 1 0 0 0 1 = 17
0 0 0 1 0 0 1 0 = 18
: :
0 0 0 1 1 1 1 1 = 31
  Address and wildcard mask:
  172.30.16.0 0.0.15.255
Notes: Slide 1 of 1
Purpose: This slide describes an example of how wildcard mask bits will match all hosts on subnets 172.30.16.0/24 to 172.30.31.0/24.
Emphasize: This process requires a thorough understanding of binary numbering, what values to use in the power of two bit positions, and how to convert a number from decimal to binary.
If some of your students seem to lack this understanding, tell them that responsibility for complex access list design is an advanced configuration skill. Later, this course offers a hands-on lab to allow practice designing simple access lists.
If you feel that your students need another example to improve their understanding of the process, prepare another example as a chalk talk. Consider having students volunteer to help as you solve your own example that lines up the binary bits of the address and the binary bits of the wildcard mask.

## Slide 26: 配置标准的 IP 访问列表
© 1999, Cisco Systems, Inc.
www.cisco.com
10-26

## Slide 27: 标准IP访问列表的配置
access-list access-list-number {permit|deny} source [mask]
Router(config)#
  为访问列表设置参数
  IP 标准访问列表编号 1 到 99
  缺省的通配符掩码 = 0.0.0.0
  “no access-list access-list-number” 命令删除访问列表
Notes: Slide 1 of 2
Purpose: This slide gives the specific command syntax for TCP/IP standard access list configuration. The access-list command creates an entry in a standard access list.
Emphasize: The access-list field descriptions:
  list—identifies the list to which the entry belongs; a number from 1 to 99.
  address—source IP address.
  wildcard-mask—identifies which bits in the address field are matched. It has a 1 in positions indicating “don't care” bits, and a 0 in any position which is to be strictly followed.

## Slide 28: 标准IP访问列表的配置
access-list access-list-number {permit|deny} source [mask]
Router(config)#
  在端口上应用访问列表
  指明是进方向还是出方向
  缺省 = 出方向
  “no ip access-group access-list-number” 命令在端口上删除访问列表
Router(config-if)#
ip access-group access-list-number { in | out }
  为访问列表设置参数
  IP 标准访问列表编号 1 到 99
  缺省的通配符掩码 = 0.0.0.0
  “no access-list access-list-number” 命令删除访问列表
Notes: Slide 2 of 2
Purpose: This layer shows the ip access-group command.
Emphasize: The ip access-group command links an access list to an interface. Only one access list per interface per direction per protocol is allowed.
The ip access-group field descriptions:
  list—number of the access-list to be linked to this interface.
  direction - default in outbound. Note: Create the access-list first before applying it to the interface. If it is applied to the interface before it is created, the action will be to permit all traffic. However, as soon as you create the first statement in the access list, the access list will be active on the interface. Since there is the implicit deny all at the end of every access list, the access-list may cause most traffic to be blocked on the interface. To remove an access-list, remove it from all the interfaces first, then remove the access-list. In older version of IOS, removing the access-list without removing it from the interface can cause problems.

## Slide 29: 标准访问列表举例 1
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 1 permit 172.16.0.0 0.0.255.255
(implicit deny all - not visible in the list)
(access-list 1 deny 0.0.0.0 255.255.255.255)
Notes: Slide 1 of 2
Purpose: This slide gives a specific TCP/IP example of a standard access list configuration.
Emphasize: Describe each part of the standard access list to your students. The blue statements represent the implicit deny all.
A good way to teach this material is to start with another similar configuration on the board. Set goals that will result in the example and have students tell you how to configure it. Have the students tell you what to write. After the configuration correct on the board, use the slide to review.

## Slide 30: 标准访问列表举例 1
  Permit my network only
access-list 1 permit 172.16.0.0 0.0.255.255
(implicit deny all - not visible in the list)
(access-list 1 deny 0.0.0.0 255.255.255.255)
interface ethernet 0
ip access-group 1 out
interface ethernet 1
ip access-group 1 out
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
Notes: Slide 2 of 2
Purpose:
Emphasize: Because of the implicit deny all, all non 172.16.x.x traffic are blocked going out E0 and E1.
Note: The red arrows represent the access-list is applied as an outbound access-list.

## Slide 31: 标准访问列表举例 2
  Deny a specific host
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 1 deny 172.16.4.13 0.0.0.0
Notes: Slide 1 of 3
Purpose: This slide gives another specific TCP/IP example of a standard access list configuration.
Emphasize:
Note: The wildcard mask of 0.0.0.0 is the default wildcard mask. It does not have to be specified.

## Slide 32: 标准访问列表举例 2
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
  Deny a specific host
access-list 1 deny 172.16.4.13 0.0.0.0
access-list 1 permit 0.0.0.0 255.255.255.255
(implicit deny all)
(access-list 1 deny 0.0.0.0 255.255.255.255)
Notes: Slide 2 of 3
Purpose:
Emphasize: Each access-list should have at least one permit statement in it to make it meaningful because of the implicit deny all statement at the end.

## Slide 33: 标准访问列表举例 2
access-list 1 deny 172.16.4.13 0.0.0.0
access-list 1 permit 0.0.0.0 255.255.255.255
(implicit deny all)
(access-list 1 deny 0.0.0.0 255.255.255.255)
interface ethernet 0
ip access-group 1 out
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
  Deny a specific host
Notes: Slide 3 of 3
Purpose:
Emphasize: Only host 172.16.4.13 is blocked from going out on E0 to subnet 172.16.3.0.
Ask the students what will happen if the access-list is placed as an input access-list on E1 instead - Host 172.16.4.13 will be blocked from going out to the Non 172.16.0.0 cloud as well as to subnet 172.16.3.0.
Note: The red arrows represent the access-list is applied as an outbound access-list.

## Slide 34: 标准访问列表举例 3
  Deny a specific subnet
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 1 deny 172.16.4.0 0.0.0.255
access-list 1 permit any
(implicit deny all) (access-list 1 deny 0.0.0.0 255.255.255.255)
Notes: Slide 1 of 2
Purpose: This slide gives another specific TCP/IP example of a standard access list configuration.
Emphasize: This example features the use of the wildcard abbreviation any.

## Slide 35: 标准访问列表举例 3
access-list 1 deny 172.16.4.0 0.0.0.255
access-list 1 permit any
(implicit deny all) (access-list 1 deny 0.0.0.0 255.255.255.255)
interface ethernet 0
ip access-group 1 out
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
  Deny a specific subnet
Notes: Slide 2 of 2
Purpose:
Emphasize: All hosts on subnet 172.16.4.0 is blocked from going out on E0 to subnet 172.16.3.0. Note: The red arrows represent the access-list is applied as an outbound access-list.

## Slide 36: 用访问列表控制vty访问
© 1999, Cisco Systems, Inc.
www.cisco.com
10-36

## Slide 37: 在路由器上过滤vty
  五个虚拟通道 (0 到 4)
  路由器的vty端口可以过滤数据
  在路由器上执行vty访问的控制
0
1
2
3
4
Virtual ports (vty 0 through 4)
Physical port e0 (Telnet)
Console port (direct connect)
console
e0
Notes: Slide 1 of 1
Purpose:
Emphasize: Instead of applying a standard access-list to a physical interface, now we will apply a standard access-list to the router’s vty ports. A vty port is a logical port on the router that can accept telnet sessions.
Note:
Access-class is used to filter incoming telnet session into the router’s vty ports and to filter outgoing telnet session from the router’s vty port.
Access-class always use standard access-list to match the source address of the incoming telnet session and the destination address of the outgoing telnet session.
The 2500 series router by default has 5 vty ports (vty 0 through 4).
To configure more vty ports, use the following global configuration command:
RouterB(config)#line vty 0 ?
<1-188> Last Line number
<cr>

## Slide 38: 如何控制vty访问
0
1
2
3
4
Virtual ports (vty 0 through 4)
Physical port (e0) (Telnet)
  使用标准访问列表语句
  用 access-class 命令应用访问列表
  在所有vty通道上设置相同的限制条件
Router#
e0
Notes: Slide 1 of 1
Purpose:
Emphasize: To filter incoming and outgoing telnet sessions to and from the router’s vty ports, standard access-list is used.
If this is to block incoming telnet sessions into a router’s vty port, the standard access-list is used to match the source address of the host trying to telnet into the router’s vty port.
If this is to block outgoing telnet sessions from the router’s vty ports to a host, the standard access-list is used to match the destination address of the host the router is trying to telnet into from its vty ports.

## Slide 39: 虚拟通道的配置
  指明vty通道的范围
  在访问列表里指明方向
access-class access-list-number {in|out}
line vty#{vty# | vty-range}
Router(config)#
Router(config-line)#
Notes: Slide 1 of 1
Purpose:
Emphasize: Use “access-class” to apply the standard access-list to the vty port. The next slide will show a configuration example.

## Slide 40: 虚拟通道访问举例
  只允许网络192.89.55.0 内的主机连接路由器的 vty 通道
access-list 12 permit 192.89.55.0 0.0.0.255
!
line vty 0 4
access-class 12 in
Controlling Inbound Access
Notes: Slide 1 of 1
Purpose: This example shows how to restrict incoming telnet sessions to the router’s vty ports.
Emphasize: The access-class is applied as an input filter.
Note: Ask the student the effect of changing the direction of the access-class to outbound instead of inbound.
Now the router can accept incoming telnet sessions to its vty ports from all hosts but will block outgoing telnet sessions from its vty ports to all hosts except hosts in network 192.89.55.0.
Once a user is telneted into a router’s vty port, the outbound access-class filter will prevent the user from telneting to other hosts as specified by the standard access-list.
Remember, when an access-list is applied to an interface, it only block or permit traffic going through the router, it does not block or permit traffic initiated from the router itself.

## Slide 41: 扩展 IP 访问列表的配置
© 1999, Cisco Systems, Inc.
www.cisco.com
10-41

## Slide 42: 标准访问列表和扩展访问列表 比较
标准
扩展
基于源地址
基于源地址和目标地址
允许和拒绝完整的
TCP/IP协议
指定TCP/IP的特定协议
和端口号
编号范围 100-199和2000-2699
编号范围 1-99和1300-1999
Notes: Slide 1 of 1
Purpose: This slide begins the discussion on extended IP access lists.
Emphasize: Distinguish the aspects of the extended IP access list from the standard access list. Your students will perform labs using extended access lists commands.
For both standard and extended IP access lists, enter an address mask that identifies which bits in the address field you want the access list to match that will be “don’t care” bit positions. For both types of access lists, the access-group command allows packet filtering into or out of the router.

## Slide 43: 扩展 IP 访问列表的配置
Router(config)#
  设置访问列表的参数
access-list access-list-number { permit | deny } protocol source source-wildcard [operator port] destination destination-wildcard [ operator port ] [ established ] [log]
Notes: Slide 1 of 2
Purpose: The access-list command creates an entry in complex traffic filter list.
Emphasize: The access-list field descriptions:
  list—a number between 100 and 199
  protocol—ip, tcp, udp, icmp, igrp, eigrp, ospf and etc……. ip = any internet protocol
    (see note below)
  source—ip address
  source-mask—wildcard-mask of address bits that must match. 0s indicate bits that must match, 1s are "don't care".
  destination—ip address
  destination-mask—wildcard-mask
  operator—lt, gt, eq, neq
  operand—a port number or application name (i.e. “23” or “telnet”)
  established-only allow established tcp session coming in (ack or rst bit must be set)
  log-generates a console message when a packet matches the access-list statement
Note:
If the protocol number is not listed, you may enter the protocol number between 1-255.

## Slide 44: 扩展 IP 访问列表的配置
Router(config-if)# ip access-group access-list-number { in | out }
  在端口上应用访问列表
Router(config)#
  设置访问列表的参数
access-list access-list-number { permit | deny } protocol source source-wildcard [operator port] destination destination-wildcard [ operator port ] [ established ] [log]
Notes: Slide 2 of 2
Purpose: Layer 2—Adds the access-group command for IP.
Emphasize:
The list number must match the number (100 to 199) you specified in the access-list command.

## Slide 45: 扩展访问列表应用举例 1
  拒绝子网172.16.4.0 的数据使用路由器e0口ftp到子网172.16.3.0
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 21
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 20
Notes: Slide 1 of 3
Purpose: This 3 layers slide shows an example of an extended IP access list.
Emphasize:

## Slide 46: 扩展访问列表应用举例 1
  拒绝子网172.16.4.0 的数据使用路由器e0口ftp到子网172.16.3.0
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 21
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 20
access-list 101 permit ip any any
(implicit deny all)
(access-list 101 deny ip 0.0.0.0 255.255.255.255 0.0.0.0 255.255.255.255)
Notes: Slide 2 of 3
Purpose:
Emphasize:. Don’t forget to include the permit statement to permit all other IP traffic out on E0.

## Slide 47: 扩展访问列表应用举例 1
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 21
access-list 101 deny tcp 172.16.4.0 0.0.0.255 172.16.3.0 0.0.0.255 eq 20
access-list 101 permit ip any any
(implicit deny all)
(access-list 101 deny ip 0.0.0.0 255.255.255.255 0.0.0.0 255.255.255.255)
interface ethernet 0
ip access-group 101 out
  拒绝子网172.16.4.0 的数据使用路由器e0口ftp到子网172.16.3.0
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
Notes: Slide 3 of 3
Purpose:
Emphasize:

## Slide 48: 扩展访问列表应用举例 2
  拒绝子网 172.16.4.0 内的主机使用路由器的 E0 端口建立Telnet会话
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 101 deny tcp 172.16.4.0 0.0.0.255 any eq 23
Notes: Slide 1 of 3
Purpose: This slide gives another example of an extended IP access list configuration.
Emphasize: Notice this example of an IP extended access list specifies a source subnet address and any destination address.

## Slide 49: 扩展访问列表应用举例 2
  拒绝子网 172.16.4.0 内的主机使用路由器的 E0 端口建立Telnet会话
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
access-list 101 deny tcp 172.16.4.0 0.0.0.255 any eq 23
access-list 101 permit ip any any
(implicit deny all)
Notes: Slide 2 of 3
Purpose:
Emphasize: Don’t forget to include the permit statement to permit all other IP traffic out on E0.

## Slide 50: 扩展访问列表应用举例 2
access-list 101 deny tcp 172.16.4.0 0.0.0.255 any eq 23
access-list 101 permit ip any any
(implicit deny all)
interface ethernet 0
ip access-group 101 out
  拒绝子网 172.16.4.0 内的主机使用路由器的 E0 端口建立Telnet会话
  允许其它数据
172.16.3.0
172.16.4.0
172.16.4.13
E0
S0
E1
Non-
172.16.0.0
Notes: Slide 3 of 3
Purpose:
Emphasize:

## Slide 51: 查看访问列表
wg_ro_a#show ip int e0
Ethernet0 is up, line protocol is up
Internet address is 10.1.1.11/24
Broadcast address is 255.255.255.255
Address determined by setup command
MTU is 1500 bytes
Helper address is not set
Directed broadcast forwarding is disabled
Outgoing access list is not set
Inbound access list is 1
Proxy ARP is enabled
Security level is default
Split horizon is enabled
ICMP redirects are always sent
ICMP unreachables are always sent
ICMP mask replies are never sent
IP fast switching is enabled
IP fast switching on the same interface is disabled
IP Feature Fast switching turbo vector
IP multicast fast switching is enabled
IP multicast distributed fast switching is disabled
<text ommitted>
Notes: Slide 1 of 1
Purpose: This slide shows how to verify an access list.
Emphasize: Lists IP interface information. Indicates whether outgoing access list is set.
Review the output of the show ip interface command. The highlighted text shows details about access list settings in the show command output.

## Slide 52: 查看访问列表的语句
    wg_ro_a#show access-lists
    Standard IP access list 1
    permit 10.2.2.1
    permit 10.3.3.1
    permit 10.4.4.1
    permit 10.5.5.1
    Extended IP access list 101
    permit tcp host 10.22.22.1 any eq telnet
    permit tcp host 10.33.33.1 any eq ftp
    permit tcp host 10.44.44.1 any eq ftp-data
    wg_ro_a#show {protocol} access-list {access-list number}
    wg_ro_a#show access-lists {access-list number}
Notes: Slide 1 of 1
Purpose: This slide introduces the show access-lists command used to verify access lists.
Emphasize: This is the most consolidated method for seeing several access lists.
Note, the implicit deny all statement is not displayed unless it is explicitly entered in the access-list.