## Slide 1: 网络地址翻译 NAT
Notes: Purpose: This chapter provides an overview of Network Address Translation (NAT) and Port Address Translation (PAT). It then discusses how to enable it on a Cisco router.
Timing: This chapter takes approximately 2 hours to present.
Note: This section has a laboratory exercise that allows students to enable NAT on a Cisco router.
Contents:
  Objectives—This section explains what the student will be able to do at the end of this chapter.
  NAT Overview—This section introduces students to NAT.
  NAT Operation—This section describes how NAT works.
  Configuring NAT—This section describes how to configure NAT on a Cisco IOS™ router.
  Verifying and Troubleshooting NAT—This section describes how to verify NAT configuration.
  Configuring and Troubleshooting PAT on the 700 Router—This section describes how to enable PAT on a 700 series Cisco router.
  Laboratory Exercise—Students will configure NAT.
  Summary—This section summarizes what was taught in the chapter.
  Review Questions—This section offers open-ended review questions. They should foster discussion after presenting the chapter.
Transition: Following are the performance objectives that describe what students will be able to do at the end of the chapter.

## Slide 2
NAT（网络地址翻译）能解决不少令人头疼的问题
它解决问题的办法是：在内部网络中使用内部地址，通过NAT把内部地址翻译成合法的IP地址，在Internet上使用
其具体的做法是把IP包内的地址池（内部本地）用合法的IP地址段（内部全局）来替换

## Slide 3
NAT 术语
NAT 功能
NAT 三种类型

## Slide 4: NAT 术语
Internet
Inside
10.1.1.1
Inside Local IP
Address
10.1.1.1
Simple NAT table
Inside Global
IP Address
166.1.1.1
10.1.1.2
Host B
172.20.7.3
A
C
B
A
B
D
SA
10.1.1.1
DA
10.1.1.1
SA
166.1.1.1
DA
166.1.1.1
D
C
Notes: Purpose: This figure is a transition into the NAT overview section. It also highlights some important NAT terms.
Emphasize: Highlight the different sending addresses on the packet before it enters the router and after it leaves the router. Compare those addresses to those listed on the NAT table.
Describe each term as it relates to the figure.
Note: The letters on the figure correspond to the descriptions in the text. Descriptions for outside local IP address and extended translation entry are not represented graphically.
Easy IP is a related feature to NAT available on Cisco routers. Configuring Easy IP is not taught in this course. The Easy IP (Phase 1) feature combines NAT and Point-to-point (PPP)/Internet Protocol Control Protocol (IPCP). This feature enables a Cisco router to automatically negotiate its own registered WAN interface IP address from a central server and enable all remote hosts to access the global Internet using this single registered IP address. Because Easy IP (Phase 1) uses existing port-level multiplexed NAT functionality within the Cisco IOS software, IP addresses on the remote LAN are invisible to the Internet.
Reference: For a complete description of the Easy IP configuration commands, refer to the “Easy IP Commands” chapter in the Dial Solutions Command Reference.

## Slide 5
内部本地地址:私有IP，不能直接用于互连网。
内部全局地址：用来代替内部本地IP地址的，对外，或在互联网上是合法的的IP地址。

## Slide 6: NAT三种类型
NAT有三种类型：静态NAT（staticNAT）、NAT池（pooledNAT）和端口NAT（PAT）。
其中静态NAT设置起来最为简单，内部网络中的每个主机都被永久映
射成 外部网络中的某个合法的地址,多用于服务器。
而NAT池则是在外部网络中定义了一系列的合法地址，采用动态分配
的方法映射到内部网络,多用于网络中的工作站。
PAT则是把内部地址映射到外部网络的一个IP地址的不同端口上。

## Slide 7: NAT静态映射实例
interface FastEthernet0/1
ip address 10.1.1.10 255.255.255.0
ip nat （指定内部接口）
!
interface Serial0/0
ip address 172.16.12.10 255.255.255.0
ip nat outside（指定外部接口）
!
ip nat inside source static 10.1.1.1 172.16.12.10
(建立两个IP地址之间的静态映射)
ip route 0.0.0.0 0.0.0.0 172.16.12.14

## Slide 8: 动态NAT的配置
ip nat pool dyn-nat 192.16.2.1 192.16.2.254 netmask 255.255.255.0
ip nat inside source list 1 pool dyn-nat
!
interface Ethernet0
ip address 10.1.1.1 255.255.255.0
ip nat inside
!
interface Serial0
ip address 192.16.2.1 255.255.255.0
ip nat outside
!
access-list 1 permit 10.1.1.0 0.0.0.255
!
Translate between inside hosts addressed from 10.1.1.0/24 to the globally unique 192.16.2.0/24 network.
This interface connected to the outside world.
This interface connected to the inside network.
Notes: Purpose: This figure displays the dynamic NAT configuration output.